## Slide 1: NetThreads: Programming NetFPGA with Threaded Software
Authors: Martin Labrecque, J. Gregory Steffan, Geoffrey Salmon, Monia Ghobadi, Yashar Ganjali
Presented by: Sarthak Jain

## Slide 2: Goals and key idea
Goal: Improve efficiency of FPGA-based systems for complex network applications
Key Idea: Use multithreaded soft processors to handle complex tasks more efficiently
Why NetFPGA?
  NetFPGA allows researchers to create custom hardware for networking tasks.
  Problem: Hardware design is hard and time-consuming
Solution: Use soft processors (programmable logic on FPGA) to make it easier.
  Easier to program (using C).
  Portable and flexible.
  Great for tasks with unpredictable processing times.

## Slide 3: NetThreads: A Multithreaded Multiprocessor System
Features:
  Multithreaded CPU design to avoid stalls and handle memory delays.
  Multiple memory types (instruction, input, output, shared) to manage limited FPGA resources.
  Supports multiple processors for scalability.
Applications: UDHCP, Packet Classification, NAT.
Challenge: Synchronization between threads is a bottleneck.

## Slide 4: Multithreaded Soft Processors
Key Idea: Run multiple threads in parallel to avoid delays.
  No need for complex hazard detection logic.
  Tolerates memory and I/O delays.
Thread Scheduling:
  De-schedule threads waiting for locks to save resources.
  Use static hazard detection to avoid data conflicts.
Memory System:
  Shared memory for multiple processors.
  DDR2 SDRAM for larger data storage.

## Slide 5: Applications & Results :: Applications Tested
UDHCP: DHCP server for 20,000 hosts.
Classifier: Deep packet inspection for HTTP traffic.
NAT: Network Address Translation with flow statistics.
Performance Results:
Throughput:
  124,000 packets/sec for small packets (64B).
  58,000 packets/sec for large packets (1518B).
Bottlenecks:
  Synchronization between threads slows things down.
  Adding a second CPU doesn’t always help due to lock contention.

## Slide 6: Challenges & Future Work
Challenges:
Synchronization is the main bottleneck.
Limited by FPGA resources (memory, clock speed).
Future Work:
Custom Accelerators: Add specialized hardware to speed up specific tasks.
Transactional Execution: Allow more threads to work in parallel, detect conflicts, and retry if needed.

## Slide 7: Conclusion
Key Takeaways:
  NetThreads makes it easier to program complex network applications on FPGAs.
  Multithreading helps handle delays and improves efficiency.
  Synchronization is a challenge, but future improvements like custom accelerators and transactional execution could help.

## Slide 8
NetThreads Architecture (2 CPUs)
CPU 1
CPU 2
Input
Buffer
(16KB)
Output
Buffer
(16KB)
Shared Memory
(Cache)
DDR2 SDRAM